## Slide 1: Minimum Energy Sub-Threshold CMOS Operation Given Yield Constraints
Max Dreo
Vincent Luu
Julian Warchall

## Slide 2: Problem Frame
- Subthreshold Operation
- Power over performance
- Threshold Voltage Variation!
- Dependent on transistor size
- Subthreshold Current:

## Slide 3: Problem Frame (cont.)
- Variation-Induced Errors
- Timing
- Functionality

## Slide 4: Problem
- To meet a given yield requirement should you
(a) increase the voltage of your subthreshold circuit's power supply,
(b) increase the size of its transistors, or
(c) use a combination of both?

## Slide 5: Ring Oscillator
-odd number of cascaded inverters using feedback
-able to determine failure automatically and apply results for a generalizable conclusion

## Slide 6: Monte Carlo Analysis
-Vary threshold voltage statistically and measure average current
and frequency
-Edited transistor model files to force first-order Vth dependence on area
-Able to determine failure when frequency is not measurable

## Slide 7: Assumptions
-As size or Vth increase, failure rates decrease exponentially:

## Slide 8: Approach
-generate failure rate graphs with simulations
-pick n and failure constraints and solve for optimal Vdd and size to minimize energy

## Slide 9: Simulations and Issues
-Technology: 90nm
-Voltage: 260-300 mV
-Size: 90-190nm
-Edited model files to include process and mismatch variations with a standard deviation of 25%.
-Inverter Chain of 101
-Only had 100 MonteCarlo sims per measurement point
-Why 101 inverters? Why 100 trials? Why 25%?
-lack of resources, had to observe enough failures in order to collect data.

## Slide 10: Voltage vs. Failure Rate

## Slide 11: Size vs. Failure Rate

## Slide 12: Conclusions and Future Work
-In the process of analyzing data.
-Want to graph voltage, size, and energy per operation based on a specific failure rate.
-Constraints caused issues in our data gathering stage.
-Redo the same simulations but with additional trials to get better data.